## Slide 1
Scope
Area of application [Freeway, Highway, Arterial]
Type of application [ATMS, ATIS]
Conceptual Specification
Type of prediction [Horizon, Step]
Traffic parameters [Flow, Speed, Occupancy, Time, Other]
Model
Methodology [Parametric, Non-parametric, Hybrid]
Type of output data [Multivariate, Multiple steps ahead predictions]
Type of input data [Multiple parameters, Temporal-spatial relationships]
Data quality

## Slide 2
Naive
[No Model Structure, No Parameters]
Ex. - Historical averages, Naive forecast
Parametric
[Predetermined structure, Parameters from data]
Ex.- ARIMA, Linear & Non-linear Regression
Non-Parametric
[Structure and parameters from data]
Ex. - Neural Networks, K- Nearest Neighbour
Hybrid

## Slide 3
Model | Characteristics | Input data | Advantages | Disadvantages
Exponential smoothing | linear | deterministic stationarity small quantity continuity | small quantity of data needed | 
ARIMA |  | stochastic non-stationarity small quantity | well established theoretical background | 
Kalman filtering |  |  | multivariate modelling | 
Nearest neighbour |  |  | simple model structure | 
Neural networks |  |  | able to map complex tempo-spatial relationships multivariate modelling accurate multistep-ahead predictions | data intensive
Support vector machines |  |  |  | 

## Slide 4
Model | ME |  | MAE |  | RMSE |  | MPE |  | MAPE | 
 | 15 min | 30 min | 15 min | 30 min | 15 min | 30 min | 15 min | 30 min | 15 min | 30 min
Historical averages | -11.50 | -22.98 | 48.15 | 93.80 | 61.76 | 120.40 | -14.12 | -14.01 | 54.79 | 53.14
Naive | -0.18 | -0.34 | 15.79 | 30.88 | 25.48 | 49.21 | -3.60 | -4.16 | 20.52 | 19.73
Linear regression | -11.06 | -22.09 | 48.08 | 93.53 | 61.81 | 120.50 |  |  | 55.36 | 53.57
ARIMA | 0.63 | 2.13 | 15.33 | 29.85 | 23.52 | 45.39 |  |  | 31.71 | 25.87
Exponential smoothing | 0.12 | 0.84 | 15.41 | 30.04 | 25.33 | 50.44 |  |  | 20.16 | 19.77
Neural network autoregressive | -0.42 | -0.29 | 16.20 | 28.93 | 24.95 | 42.96 |  |  | 18.65 | 16.62
K-nearest neighbour |  |  | 14.24 | 25.78 | 20.73 | 39.00 |  |  | 17.44 | 15.10
Support vector regression |  |  | 16.26 | 32.79 | 21.33 | 42.55 |  |  | 31.48 | 30.19
Simple RNN |  |  | 13.87 | 25.81 | 19.99 | 36.86 |  |  | 17.41 | 16.05
GRU |  |  | 14.21 | 27.85 | 20.31 | 39.59 |  |  | 18.14 | 18.62
LSTM |  |  | 13.97 | 31.12 | 20.28 | 42.69 |  |  | 17.64 | 19.16
LSTM (Multiple locations) |  |  | 15.14 | 18.25 | 21.90 | 25.36 |  |  | 17.77 | 21.78

## Slide 6
Vehicle induced currents
Inductive loop wire
Reinforcing steel mesh or rebar
Pull box
Lead in wire
Lead in cable
Controller cabinet
Electronic unit containing tuning network, oscillator and sensitivity settings
Presence or pulse output