## Slide 1
Scope
Area of application [Freeway, Highway, Arterial]
Type of application [ATMS, ATIS]
Conceptual Specification
Type of prediction [Horizon, Step]
Traffic parameters [Flow, Speed, Occupancy, Time, Other]
Model
Methodology [Parametric, Non-parametric, Hybrid]
Type of output data [Multivariate, Multiple steps ahead predictions]
Type of input data [Multiple parameters, Temporal-spatial relationships]
Data quality

## Slide 2
Naive
[No Model Structure, No Parameters]
Ex. - Historical averages, Naive forecast
Parametric
[Predetermined structure, Parameters from data]
Ex.- ARIMA, Linear & Non-linear Regression
Non-Parametric
[Structure and parameters from data]
Ex. - Neural Networks, K- Nearest Neighbour
Hybrid

## Slide 3
Model | Model characteristics | Data characteristics | Advantages | Disadvantages
Exponential smoothing | linear | deterministic stationarity small quantity continuity | small quantity of data needed | 
ARIMA |  | stochastic non-stationarity small quantity | well established theoretical background | focus on mean, miss the extremes sensitive to missing data
Kalman filtering |  |  | multivariate modelling | 
Nearest neighbour |  |  | simple model structure multivariate modelling robustness to missing data | 
Neural networks |  |  | able to map complex tempo-spatial relationships multivariate modelling accurate multistep-ahead predictions robustness to missing data | data and computation intensive
Bayesian networks |  |  | multivariate modelling | 
Support vector machines |  |  |  | 

## Slide 4
Model | MAE |  |  | RMSE |  |  | MAPE |  | 
 | 15 min | 30 min | 45 min | 15 min | 30 min | 45 min | 15 min | 30 min | 45 min
Naive | 22.98 | 44.87 | 71.35 | 33.15 | 65.62 | 104.70 | 13.75 | 14.05 | 15.74
Linear regression | 52.73 | 101 | 148.2 | 78.59 | 154 | 228.8 | 28.63 | 27.54 | 27.11
ARIMA | 21.20 | 39.76 | 62.85 | 29.93 | 57.09 | 88.52 | 12.42 | 11.87 | 12.56
Exponential smoothing using state space model | 21.61 | 42.25 | 67.25 | 31.12 | 61.51 | 96.83 | 12.87 | 12.95 | 14.23
Neural network autoregressive | 17.98 | 30.01 | 42.27 | 24.85 | 41.23 | 56.73 | 11.34 | 10.04 | 9.88
K-nearest neighbour | 17.96 |  |  | 26.07 |  |  | 11.74 |  | 
Support vector regression |  |  |  |  |  |  |  |  | 
Deep RNN (Vanilla) | 24.73 |  |  | 33.52 |  |  | 15.91 |  | 
Deep GRU | 23.01 |  |  | 32.47 |  |  | 13.69 |  | 
Deep LSTM | 23.62 |  |  | 33.44 |  |  | 15.87 |  | 
Deep LSTM (Multivariate) |  |  |  |  |  |  |  |  | 
Table showing the test accuracies when predicting for the month of June 2013

## Slide 5
Day | Date | Time | Severity
Monday | 01/08/2010 | 01.24 | Other injury
Wednesday | 10/11/2010 | 13.00 | Other injury
Friday | 12/11/2010 | 22.00 | Other injury
Saturday | 18/01/2011 | 21.30 | Other injury
Monday | 07/03/2011 | 07.38 | Serious injury
Wednesday | 11/05/2011 | 12.30 | Other injury
Saturday | 21/05/2011 | 01.30 | Serious injury
Wednesday | 28/09/2011 | 10.20 | Other injury
Friday | 16/03/2012 | 17.30 | Serious injury
Tuesday | 24/07/2012 | 14.50 | Other injury
Wednesday | 10/10/2012 | 14.40 | Other injury
Friday | 02/11/2012 | 15.18 | Other injury
Saturday | 17/11/2012 | 23.35 | Other injury
Friday | 30/11/2012 | 23.05 | Serious injury
Friday | 15/03/2013 | 10.40 | Other injury
Wednesday | 15/05/2013 | 20.00 | Other injury
Wednesday | 03/07/2013 | 13.30 | Other injury
Wednesday | 28/08/2013 | 13.50 | Other injury

## Slide 6
Day | Date | Holiday
Monday | 02/01/2012 | New year’s day (in lieu)
Thursday | 26/01/2012 | Australia day
Monday | 12/01/2012 | Labour day
Friday | 06/04/2012 | Good Friday
Monday | 09/04/2012 | Easter Monday
Wednesday | 25/04/2012 | ANZAC day
Monday | 11/06/2012 | Queen’s birthday
Tuesday | 06/11/2012 | Melbourne cup day
Tuesday | 25/12/2012 | Christmas day
Wednesday | 26/12/2012 | Boxing day

## Slide 8
Vehicle induced currents
Inductive loop wire
Reinforcing steel mesh or rebar
Pull box
Lead in wire
Lead in cable
Controller cabinet
Electronic unit containing tuning network, oscillator and sensitivity settings
Presence or pulse output